## Slide 1
DS252 · INTRODUCTION TO CLOUD COMPUTING
Lance
Leased authority for agentic ground-robot navigation across edge and cloud
Deciding where the decision is made
And what happens when the link degrades
Team Nimbus

## Slide 2
THE SETTING
The real question: who decides, and for how long
A SunFounder PiCar-X runs fixed-map errands indoors and outdoors — carrying a sample, fetching an item — among obstacles that are not fixed: a person crossing a corridor, a chair pulled out, a trolley left overnight.
Finding the route is cheap and cached. The hard question is runtime: when something unexpected appears, who is allowed to decide what to do about it, on what evidence, for how long?
<100ms
Swerve around a person
A local decision — must complete instantly
~1s
Wait, retry, or ask for help
The band that is neither local nor global
Several s
Abandon the corridor, re-route
A global decision — needs the map and mission history
Nimbus
02 / 17

## Slide 3
Why both extremes fail under an unstable link
FAILS AS THE LINK DEGRADES
Cloud-authoritative control
Every tactical decision pays a wide-area round trip plus multi-second LLM inference — and gets slower exactly when the link gets worse.
REMOVES OVERSIGHT
Unbounded edge autonomy
Removes the network dependency, but also the global knowledge, semantic map and mission history that only the cloud holds. Further may be a compromise on performance of models.
Neither language model can be the controller: a 1–3B edge SLM still costs about a second per decision, so reflex and reactive avoidance stay classical, and the language models are confined to the bands their latency can afford. The goal would be to use intelligence provided by these models while ensuring quick action.
Nimbus
03 / 17

## Slide 4
THE IDEA
An authority lease: a time- and space-bounded grant from cloud to edge
Corridor
A connected sub-graph of the fixed map the edge may act inside
TTL
A time limit; authority decays on a schedule, not by surprise
Guards
Max speed, min clearance, geo-fence, max deviation
Epoch · seq
Every command is idempotent; stale or duplicate commands are rejected
Nimbus
04 / 17

## Slide 5
Four control bands, one architecture
LAN BOUNDARY
WAN BOUNDARY
R0
Reflex gate
No network, no model — clamps speed on an ultrasonic or cliff breach
DEVICE
R1
Reactive avoidance
Classical DWA-class controller over a local occupancy window — no language model on this path
EDGE
R2
Tactical SLM arbiter
Triggered only; ≤32-token schema-checked decision — continue, branch, wait, escalate or hold
EDGE
R3
Deliberative planner
Cloud LLM plans routes, issues authority leases, replans on escalation
CLOUD
Nimbus
05 / 17

## Slide 6
The degradation ladder
Lease age converts into a bounded reduction of authority — never a surprise, always the same five rungs.
L0 · NORMAL
age < renew_at
Full speed & corridor, renewals on schedule
L1 · SOFT
renew_at ≤ age < ttl
Speed halved, no new branch choices
L2 · HARD
age ≥ ttl
Proceeds only to the nearest hold point
L3 · SAFE-HOLD
at hold point, or guard trip
Motors disabled, telemetry buffered
RESYNC
link restored
Pose & epoch validated, fresh lease issued
Nimbus
06 / 17

## Slide 7
Three configurations, one codebase
Selectable by a single policy flag. The wider M1 / M2 sweep from the original design was dropped from this revision to keep the campaign focused on the floor, the proposal and the baseline.
Config | Decision path | Where it wins | Cost driver
M0 · Classical floor | Reflex + reactive only, precomputed route — no language model anywhere | Safety and cost floor; always available | None
M3+ · Leased authority (proposed) | SLM decides inside lease bounds; cloud plans and renews rarely | Holds the frontier as the link degrades | Tokens only at plan / replan time
M4 · Cloud-authoritative | Every tactical decision goes to the cloud LLM | Simplest to reason about on a stable link | Dominated by the token term
Nimbus
07 / 17

## Slide 8
Scope: in, out, and the MVP
In scope
Lease control plane: issue, renew, escalate, revoke, resync
Four-band control stack
Degradation ladder
Cloud-resident map & mission state on AWS
API Gateway remote-control front door
Three arbitration models + no-LLM floor
Fault injection, workload generator, evidence pipeline
Out of scope
Zero-connectivity operation as a design goal
SLAM research (fiducial localisation only)
A physical multi-robot fleet
Training or fine-tuning any model
Modifying the PiCar-X chassis or sensors
Formal safety certification
Centimetre-grade positioning
MVP
FR-1 to FR-7 and NFR-1 to NFR-7, configurations M0, M3+ and M4, run primarily in Gazebo simulation.
PiCar-X hardware validation moves to Stretch
Nimbus
08 / 17

## Slide 9
What must be true: the MVP requirements
FR-1 to FR-7 and NFR-1 to NFR-7 — the requirement set behind the MVP scope
FUNCTIONAL — WHAT IT MUST DO
FR-1
Device reflex gate — clamps speed, no network or model
FR-2
Edge reactive avoidance — classical, no LLM on this path
FR-3
Plan & lease issue — route + schema-validated lease
FR-4
Prefetch-on-lease — map tiles ship with the lease
FR-5
Tactical SLM arbiter — ≤32-token schema-checked decision
FR-6
Escalation path — compact delta, never improvised
FR-7
Degradation ladder — lease age maps to L0–L3
NON-FUNCTIONAL — MVP TARGETS
≤100ms p99
NFR-1 · breach to zero-velocity command
≤200ms p95
NFR-2 · perception frame to revised segment
≤1.2s p95
NFR-3 · SLM decision, 32-token cap
≤8s p95
NFR-4 · plan + lease committed
≤400ms p95
NFR-5 · lease renewal round trip, no LLM
Zero collisions
NFR-6 · across 50 injected instability episodes
100% rejection
NFR-7 · duplicated, reordered, stale-epoch commands
Nimbus
09 / 17

## Slide 10
Experiments and evidence
E1 · Nominal campaign
Success, latency and cost across all configs and link profiles
E2 · Dynamic obstacles
Isolates what the tactical band adds over classical avoidance
E3 · Degraded-link sweep
Configs under P1/P2, plus the lease-context ablation
E4 · Instability & recovery
Ladder transitions, collisions, RPO and RTO under P3/P4
E5 · Idempotency
500-message replay with duplication, reorder and epoch rollback
E6 · Safety floor
Reflex cutoff latency, sim and hardware, edge and cloud black-holed
E7 · Elasticity
Synthetic fleet at 1, 10, 25 robots loads the cloud tier
E8 · Red team
20 adversarial scenes; prompt-injection and forged-marker resistance
Nimbus
10 / 17

## Slide 11
WITHIN CURRENT SCOPE
Nimbus in action: a sample errand
In the app:
Bench 2
Bench 5
Send errand
1
Requester asks
Natural-language errand, Bench 2 to Bench 5, typed into the app
2
Cloud plans & leases
Route plus a 20s-TTL lease for the corridor; map tiles prefetched
3
Obstacle, handled locally
A person crosses; the edge reactive layer avoids it, no cloud call
4
Lease renews
Four renewals along the way — control-plane pings, zero LLM calls
5
Arrival
One LLM call billed for the whole errand
Nimbus
11 / 17

## Slide 12
NOT IN THE CURRENT PROPOSAL
Beyond this proposal: where the lease generalises
The lease is a generic authority abstraction, not an errand-specific one — FR-14's stretch reminder capability already tests that on the unchanged lease schema.
More errand types
New guard sets and action schemas on the same lease machinery, no control-loop change
A physical multi-robot fleet
The lease plane is already load-tested against a synthetic fleet of 25
Other mobile platforms
Any platform with a reflex / reactive / tactical / deliberative split — warehouse AMRs, drones
A safety-certification path
Once E6 / E8's safety-floor and red-team evidence is established
A multi-tenant cloud service
Beyond a single AWS account — per-tenant isolation and billing
Nimbus
12 / 17

## Slide 13
WHAT WE ENVISION
Different errands, one question: why even the cloud?
Same lease machinery throughout — what changes is how much of the errand only a real language model can work out
NAVIGATION
“Bench 2 to Bench 5”
A fixed pickup and a fixed drop — the tactical SLM handles almost all of it
REASONING NEEDED
FR-14 · REMINDER
“Tell Dr. Rao at his desk about the 3pm meeting”
Cloud resolves “Dr. Rao’s desk” to a marker and composes the message once
REASONING NEEDED
CONDITIONAL
“If Bench 3 is busy, leave it at Bench 4 instead”
A branching instruction — the arbiter has to judge the scene, not just steer
REASONING NEEDED
AMBIGUOUS
“Fetch whichever sample is ready first — ask me if you're not sure”
Open-ended intent, real judgement, maybe a clarifying question — only an LLM, not a 1–3B SLM, can carry this
REASONING NEEDED
Pure navigation might get by without the cloud. The moment an errand carries open-ended human intent, it needs a real language model — which is exactly why the deliberative tier, and the lease that bounds it, exist.
Nimbus
13 / 17

## Slide 14
Team and module ownership
Every module has a lead; the heavier modules are shared
Module | Person1 | Person2 | Person3 | Person4
Platform & simulator foundation | — | — | — | Lead
Edge perception & reactive avoidance | Lead | — | Support | —
Cloud lease plane & planner | — | Support | Lead | —
Tactical arbiter & degradation ladder | Lead | — | — | Support
Configurations, cost & fleet campaign | Shared | Shared | Shared | Shared
Hardware validation, red team & report | — | Lead | — | —
Nimbus
14 / 17
YET TO BE DISCUSSED

## Slide 15
Project timeline
7 Sep team formation — 28 Nov final demo
WEEKS 1–3
Foundation
PiCar-X calibration, simulator skeleton, reflex gate, AWS & Terraform setup
WEEKS 4–5
Core loop
Lease plane live, edge reactive avoidance, M0 running end to end
WEEKS 6–8
Full stack
Tactical arbiter, degradation ladder, all configs behind the flag, campaign begins
WEEKS 9–10+
Evidence & demo
Hardware validation, red team, analysis, report, final demo
MS1 (end Wk 2): reflex gate cuts motors live, edge & cloud black-holed
MS2 (end Wk 4): lease issued, ladder steps L1→L3 live on Grafana
MS3 (end Wk 6): full campaign, cost frontier, live hardware errand
Nimbus
15 / 17

## Slide 16
Risks and mitigations
R1
The edge SLM is too slow for NFR-3
Plan B: fall back to a lightweight classifier over the same action set, or shift tactical reasoning to the cloud — the lease machinery and every experiment stay unchanged.
R2
AWS spend or LLM rate limits overrun budget
Budget alarms and cost tags from Week 1, a mock planner for latency-insensitive cells, low replica floors, weekly teardown checks.
R3
The campaign does not fit the schedule
A declared reduction order — stretch cells first, then long outages, then M1 — but never the safety experiments E4, E5, E6.
Nimbus
16 / 17

## Slide 17
SUMMARY
Authority decays safely when connectivity does — measured, not assumed
7 FRs / 7 NFRs
MVP requirement set
M0 / M3+ / M4
Configurations measured
Gazebo-first
Hardware in Stretch
Thank you — questions welcome